## Slide 1: CAN Driver
By
Laxmi Gangal
Nisarga Hanji

## Slide 2: CAN Protocol
Controller Area Network
Invented by Robert Bosch in 1980 for automotive applications
Asynchronous Serial Bus
Simple 2-wire differential bus
Absence of node addressing
Message identifier specifies contents and priority
Lowest message identifier has highest priority
Sophisticated error detection and handling system

## Slide 3: APIs for CAN Driver
Initialization function
Enable CAN clock in the power control for peripherals [PCONP] register.
void CAN1_Init(void)
Power on CAN1
PCLK_CAN1=CCLK/1

## Slide 4: Initialization API:
void CAN1_Init(void)
* @brief the Initialization of CAN
* @param : none
* return none

## Slide 5: APIs for CAN Driver
Configure CAN pins
The CAN1 module is typically on P0.0 (RD1) and P0.1 (TD1).
These can be set as CAN1_RX and CAN1_TX.
void CAN1_PinConfig(void)
set CAN1 functionality
Set P0.0 as RD1 and P0.1 as TD1 in Pin Function Select Register [PINSEL0].

## Slide 6: Pin configuration API:
void CAN1_PinConfig(void)
* @brief the pin configuration of CAN
* @param : none
* return none

## Slide 7: APIs for CAN Driver
Set CAN Baud Rate
It depends on CAN clock [PCLK] and CAN Bus Timing Register [CANBTR]
The CANBTR is configured based on Baud Rate Prescalar [BRP] , TSEG1, TSEG2 and Synchronization Jump Width [SJW].
void CAN1_SetBaudRate(void)
Example: for 500kbps
(TSEG1 = 4, TSEG2 = 3, SJW = 1, BRP = 4, PCLK=25MHz)
Baud Rate= PCLK/(BRP + 1) (TSEG1 + TSEG2 + 1)

## Slide 8: Baud Rate API:
void CAN1_SetBaudRate(uint32_t baudrate, uint32_t pclk)
* @brief the Baud rate of CAN
*@param baud : the baud rate of the CAN data to be transmitted
* valid values: 125 ...100000 in kbps
*@param clock: the peripheral clock frequency in MHz
* valid values: 100 MHz, 50 MHz, 25 MHz, 12.5 MHz
* return none

## Slide 9: APIs for CAN Driver
Transmit a CAN message
Load data into a transmit buffer
Set message ID and control bits
Enable transmission
void CAN1_Transmit(uint32_t id, uint8_t *data, uint8_t len)
CAN Transmit Frame Information Register [CAN1TFI]
CAN Transfer Identifier [CAN1TID]
CAN Transmit Data Register [CAN1TDA]
CAN Command Register [CAN1CMR]

## Slide 10: Transmit API:
void CAN1_Transmit (uint32_t id, uint8_t *data, uint8_t len)
* @brief the data transmitted from CAN
*@param id: CAN Message ID (Standard: 11-bit, Extended: 29-bit).
* valid values: Standard Id- 0x000 to 0x7FF
Extended Id- 0x00000000 to 0x1FFFFFFF
*@param data: Pointer to the data buffer
* valid values: any data of 0 to 8 bytes
*@param len : Number of bytes in the CAN message
* valid values: 0 to 8
*return none