## Slide 1: CAN Driver
By
Laxmi Gangal
Nisarga Hanji

## Slide 2: CAN Protocol
Controller Area Network
Invented by Robert Bosch in 1980 for automotive applications
Asynchronous Serial Bus
Simple 2-wire differential bus
Absence of node addressing
Message identifier specifies contents and priority
Lowest message identifier has highest priority
Sophisticated error detection and handling system

## Slide 3: APIs for CAN Driver
Initialization function
Enable CAN clock in the power control for peripherals [PCONP] register.
void CAN_Init(uint8_t CAN_idx)
Power on CAN

## Slide 4: Initialization API:
void CAN_Init(uint8_t CAN_idx)
* @brief the Initialization of CAN
*@param idx: index to the CAN.
*@valid values: 1 - CAN1
2 – CAN2
* return none

## Slide 5: APIs for CAN Driver
Set CAN Baud Rate
It depends on CAN clock [PCLK] and CAN Bus Timing Register [CANBTR]
The CANBTR is configured based on Baud Rate Prescalar [BRP] , TSEG1, TSEG2 and Synchronization Jump Width [SJW].
void CAN_SetBaudRate(uint8_t CAN_idx, uint16_t BaudRate_Kbps)

## Slide 6: Baud Rate API:
void CAN_SetBaudRate( uint8_t CAN_idx, uint16_t BaudRate_Kbps )
*@brief the Baud rate of CAN
*@param idx: index to CAN
*@valid values: 1 - CAN1
2 - CAN2
*@param baud : the baud rate of the CAN data to be transmitted
* valid values: 125, 250, 500, 1000 in kbps
* return none

## Slide 7: APIs for CAN Driver
Transmit a CAN message
Check if the transmit buffer is free
Load data into a transmit buffer
Set message ID and control bits
start transmission
void CAN_Transmit(uint8_t CAN_idx, uint32_t id, uint8_t *data, uint8_t len)
CAN Transmit Frame Information Register [CANTFI]
CAN Transfer Identifier [CANTID]
CAN Transmit Data Register [CANTDA]
CAN Command Register [CANCMR]

## Slide 8: Transmit API:
void CAN_Transmit (uint8_t idx, uint32_t id, uint8_t *data, uint8_t len)
* @brief the data transmitted from CAN
*@param idx: index to CAN
*@valid values: 1 - CAN1
2 - CAN2
*@param id: CAN Message ID (Standard: 11-bit, Extended: 29-bit).
*valid values: Standard Id- 0x000 to 0x7FF
Extended Id- 0x00000000 to 0x1FFFFFFF
*@param data: Pointer to the data buffer
* valid values: any data of 0 to 8 bytes
*@param len : Number of bytes in the CAN message
* valid values: 0 to 8
*return none

## Slide 9: APIs for CAN Driver
Receive a CAN message
Check for new message
Extract ID & DLC
Read data
Release buffer
void CAN_Receive(uint8_t CAN_idx, uint32_t *id, uint8_t *data, uint8_t len)
CAN Receive Frame Information Register [CANRFS]
CAN Receive Data Registers[CANRDA, CANRDB]
CAN Command Register [CANCMR]

## Slide 10: Receive API:
Void CAN_Receive(uint8_t CAN_idx, uint32_t *id, uint8_t *data, uint8_t *len)
*@brief Receives a message from the CAN
*@param idx: index to CAN
*@valid values: 1 - CAN1
2 - CAN2
*@param id: Pointer to store the received CAN Message ID
* valid values: Standard Id- 0x000 to 0x7FF
Extended Id- 0x00000000 to 0x1FFFFFFF
*@param data: Pointer to the data buffer to store received bytes.
* valid values: any data of 0 to 8 bytes
*@param len: Number of bytes received (DLC value)
* valid values: 0 to 8
* return none